WARNING NOTICE

Dear IMMERSTAR Owner;

You have just purchased an alarm device for swimming pools that complies with the French standard NFP 90-307/A1:

This system is not a substitute for common sense or for individual responsibility.

The safety of your children depends on you alone! The risk is greatest when your children are under 5 years of age.

Accidents do not only happen to others! Be ready to act! In no case can ACIS be held responsible for any fall or drowning of any person or animal.

Use of the IMMERSTAR device must not lessen your vigilance or substitute for active supervision of the pool and its surroundings.

Warranty: In order to benefit fully from the IMMERSTAR warranty, it is imperative that you fill in and sign the warranty card provided, and return it within 8 days to ACIS, 2, rue du Port 85230 BEAUVOIR SUR MER (France) by traceable mail (registered letter with acknowledgement of receipt, traceable mail).

The warranty on the IMMERSTAR alarm does not come into force until receipt of the properly filled in warranty card.

If this card is not returned, no warranty will be granted.

Carefully read through all documents relating to your IMMERSTAR alarm and keep them at hand for further consultation.

Table of Contents

Presentation

System for detecting the immersion or fall of a corps adaptable on the edge of in-ground, semi-in-ground or above-ground swimming pools maximum 12 x 5 in size (range: 7 metres).

Beyond that, we recommend equipping the pool with additional protective measures compliant to the French standard NF P90-307/A1.

In compliance with the standard NFP 90-307/A1, your alarm is configured for a rectangular pool 4 x 8 m in size and 1.40 m depth (the most widely used type of pool in France).

IMMERSTAR can be used in pools up to 5 x 12 m in size.

IMMERSTAR analyzes the movement of the water in your pool and knows how to distinguish interference waves (cascade, filtration, rain, wind) from those emitted by the falling of a body. The response time is proportional to the distance between the point of detection and the point of immersion.

Warning! The installation and use of an alarm system is no substitute for your personal vigilance. The IMMERSTAR is an additional tool to human vigilance for supervision of pools.

This method is no substitute for the attention of adults.

Supervise your children carefully!

Limits of Use

• You can use the IMMERSTAR alarm only if the pool installation allows complete intervention (including rescuing in the pool) in under 3 minutes from the house or place of accommodation.

• The standard NFP 90-307/A1 relating to pool alarms specifies the detection of any fall within a maximum delay of 12 seconds: therefore the IMMERSTAR may not be situated more than 7 metres away from any potential fall site.

In order to make large sized pools compliant, you could be obliged to install one or more additional IMMERSTAR alarms.

• The safety, alarm and fault signals must be audible from the house or place of accommodation. This must be verified during installation.

• Shape and equipment of the pool: For pools of unique shape or in the case of large pools (close to 12 x 5 metres), only an onsite test can verify the compatibility of the IMMERSTAR with your equipment.

Warning: some pool equipment may be incompatible with the proper functioning of the IMMERSTAR alarm (pool covering, cleaning robot…).

Ask your installer for advice.

• The IMMERSTAR alarm is not designed for self-supporting pools with soft walls, pools without a border, mirror pools, pools equipped with a gradually sloped access or pools equipped with a high rate of filtration (similar to that of a counter-current system). The use of a bubble cover can impede the functioning of the IMMERSTAR alarm.

• In surveillance mode, the IMMERSTAR alarm device adapts its sensitivity to the agitation conditions in the pool. Its sensitivity can be diminished in the case of very strong winds, storms or bad weather conditions. The wind tests were performed according to the methods specified by the standard NF P90-307/A1. Be extra vigilant if there is strong wind, gusts of wind or bad weather conditions that could affect the sensitivity of your IMMERSTAR alarm.

Checking the Packaging and Contents

Despite all care we take in the quality of our products and their packaging, we ask you to check the contents and the condition of your IMMERSTAR alarm device.

The package should contain:

A - A plate with a circuit board, with 100 dB siren, contactor with lock and battery compartment,

B - IMMERSTAR housing,

E - A blister of 4 professional alkaline batteries,

F - 2 contact keys,

F - 2 control magnets,

A plastic bag containing:

H - 4 plastic pegs,

J - 4 square steel nuts,

K - 4 steel screws 4 x 20 mm,

L - 4 steel screws 4 x 30 mm,

M - 2 steel screws 4 x 40 mm,

N - 2 steel screws 4 x 50 mm,

P - 4 soft washers,

Q - 4 spacers for adaptation to all kinds of border,

R - An installation and operation manual,

S - A warranty card to fill in and return for the warranty to be valid.

Checks Before Putting into Operation

IMMERSTAR alarm systems are tested at every stage of their manufacture.

Nevertheless, despite the care we take, if a device has been damaged upon shipping, storage or any other handling that could affect its components, only a test during installation can assure that it works properly.

Put the 4 supplied alkaline batteries into your IMMERSTAR alarm, making sure to get the polarity right.

The compartment is designed to lock the batteries in working position: clip them into place by pressing them firmly with your thumb.

Insert batteries

PRESS + CLICK

Attach the plunger tube to the IMMERSTAR alarm, not forgetting the O-ring (see diagram).

1 - Put your detector on the edge of a table or bench, for example.

2 - Switch the alarm on using one of the keys.

Observe:

3 - Red and green diodes blink alternately:
IMMERSTAR is currently in its calibration phase

+/- 3 seconds

BEEP BEEP BEEP

4 - After 3 seconds, IMMERSTAR emits a series of BEEPS: IMMERSTAR has just swapped automatically to swimming mode

5 - The green diode blinks, signalling that the IMMERSTAR is in swimming mode

+/- 3 minutes

BEEP BEEP BEEP

6 - After about 3 seconds, IMMERSTAR emits a series of BEEPS: IMMERSTAR has just swapped automatically to surveillance mode

7 - The red diode blinks, signalling that the IMMERSTAR is in surveillance mode

You will now artificially trigger the alarm. Warn everyone within earshot – the siren is loud!

Alarm in surveillance mode

Repeat up-and-down movement 4 times

1 - Immerse the tube into a bucket of water, then make an alternating up-and-down movement of the alarm (about 4 times up and down)

2 - The siren should go off. You can stop it by switching the alarm off with the key.

If the test is successful, then your immersion detector is ready to be installed.

If the test failed, check to make sure the batteries are correctly in place and then repeat the test. If the problem persists, get in touch with your vendor or ACIS.

Choice of Installation

In order to minimize the alarm’s response time in the event of a fall, the IMMERSTAR device must be fastened at the middle of the longer edge of your pool and have the entire pool in direct line of sight.

• The alarm is designed to be fastened to the border (the curvature of the cover matches the profile of classical borders; the spacers can be used to compensate for gaps).

The safety, alarm and fault signals must be audible from the house or place of accommodation. This must be verified during installation.

• Install permanent notices that the pool and its surroundings are under electronic surveillance.

• Install your IMMERSTAR device more than one metre away from any recirculation ducts, skimmers, waterfalls or other equipment that generates noise in the pool.

• Keep the access to the control zone (magnetic sector) of the IMMERSTAR free and clear.

7 metres

Installation on the Border

It is preferable to call in a professional to install and maintain the alarm system.

In accordance with specifications of the standard NF P90-307/A1, your IMMERSTAR device must be fastened in such a way that it cannot be removed by bare hands alone.

Your IMMERSTAR alarm must be firmly fastened to the border of your pool.

The IMMERSTAR alarm is equipped with pre-drilled holes and spacers for fastening it solidly to your pool border (minimum width: 100 mm).

Verify that the support (border, terrace…) is truly stable, since the IMMERSTAR must not vibrate for it to work optimally.

The alarm must be installed under no stress, with the cover removed.

Position the alarm in such a way that the plunger tube is minimum 5 mm away from the edge of the border. The IMMERSTAR alarm is designed to be fastened to rigid borders at least 100 mm wide.

• Of the 6 possible fixation points, you must use at least 4.

You can choose to use the spacers (Q) or not in order to obtain the most sturdy fixation possible.

The tube of the sensor must be vertical.

• Drill holes and insert pegs (in cement borders only)

• The foam rubber washers (P) go directly underneath the housing, or underneath the spacers if the latter are used.

• Screw the alarm onto the border using the 4 screws of the right length.

• Put the cover in place and screw it on with the four square nuts (J) and four 4 x 20 mm steel screws (K).

Functional Test in the Pool:

In order to perform this test, the following conditions must be satisfied:

• The alarm is fastened to the border

• The water in the pool is still

• It has been more than twenty minutes since the last swimmer got out of the pool

• It is a non-windy day

1. Turn your pool’s filtration system on.

2. Turn the key to switch the alarm on.

3. Red and green diodes blink alternately:

IMMERSTAR is currently in its calibration phase

4. After 3 seconds, IMMERSTAR emits a series of BEEPS: IMMERSTAR has just swapped automatically to swimming mode

+/- 3 seconds

5. The green diode blinks, signalling that the IMMERSTAR is in swimming mode

BEEP BEEP BEEP

6. After less than 15 minutes, IMMERSTAR emits a series of BEEPS:

IMMERSTAR has just swapped automatically to surveillance mode

< 15 minutes

7. The red diode blinks, signalling that the IMMERSTAR is in surveillance mode

BEEP BEEP BEEP

8. Throw a weight of about 8 kg into the pool

8 kg

9. The siren should go off. Turn it off by placing the magnet on its emplacement, or by switching the alarm off by the key.

TWEEET!

Note: if your alarm does not succeed in detecting the fall in less than 12 seconds, it may be necessary to shorten the plunger tube.

If this turns out to be necessary, only cut the tube by 2 cm at a time, and repeat the test after each cut.

In any case, the end of the plunger tube must still be more than 18 cm beneath the water.

It is also necessary to take into account the possibility of a low water level during periods of high evaporation.

| Test result | Valid | Action |
| --- | --- | --- |
| The fall is detected in less than 12 seconds (maximum) | Yes | Stop the siren |
| It takes more than 12 seconds to detect the fall | No | Repeat the test or contact your vendor or ACIS, if you prefer. |
| The fall is not detected | No |  |

At the end of the tests, the IMMERSTAR alarm will automatically return to surveillance mode once the pool water has become still again, which can take up to 12 minutes.

As it swaps to surveillance mode, the alarm emits a series of beeps in quick succession and the red LED starts to blink.

Alkaline Batteries

Despite all care taken in the choice of batteries, it can happen that unforeseeable storage may have weakened their performance. If the batteries are weak, three very quick “beeps” will sound every 40 seconds or so until the batteries have been changed.

The batteries are guaranteed to last 3 years under normal utilization (that is, no excessive triggering of the alarm).

When replacing them, always use batteries of the exact same characteristics and power. So as not to pollute the environment, return dead batteries to a proper reprocessing centre (waste collection site, recycling point).

Operation (use the table of controls given on the last page of this document)

In order to get the best satisfaction out of your alarm, familiarize yourself with the start/stop commands.

Under normal operation, it is imperative to remove the key.

So that people can swim in the pool, the IMMERSTAR alarm must be in “swimming” mode, with the green diode blinking.

If the red diode is blinking, you can switch the alarm to “swimming” mode by placing the magnet on its emplacement.

A “beep” indicates the mode change.

After swimming, the IMMERSTAR alarm automatically returns to “surveillance” mode if the water remains still for at least 2 minutes.

This automatic return to surveillance mode is indicated by multiple series of “beeps”.

Note that these must be two consecutive minutes of still water.

All things considered, the automatic activation of surveillance mode can sometimes take up to 15 minutes.

During this time, you must ensure heightened human vigilance.

It is possible to prompt a quicker return to “surveillance” mode by placing the magnet on its emplacement for a few seconds.

If the pool water is still moving too much, the alarm could refuse to be forced to return to “surveillance” mode.

Some counter-current systems prevent the automatic reactivation of the immersion detection system.

If the siren goes off, take immediate action at the accident.

You can turn off the sound of the siren by placing the magnet on the magnetic zone or by switching the alarm off with the key.

By default, the siren will sound continuously for 2 minutes, then in intermittent rounds for another 3 minutes, and then the alarm will return automatically to swimming mode.

Wintering

In order to maintain surveillance when the level of the pool has dropped over winter, equip your alarm with a wintering extension.

Contact your vendor to procure one.

Complete stop*

If you wish to stop your IMMERSTAR alarm despite the risk of interrupting the surveillance, turn the key to the OFF position and remove it from the keyhole.

Keep it in a safe place easy to remember (on a hook in your pool house, for example).

If the alarm will be deactivated for an extended period, it is recommended to remove the batteries and store them in a cool, dry place.

In order to restart your IMMERSTAR alarm, proceed from point 1 of these directions.

If you have any problems, get in touch with your vendor immediately, or ACIS if you prefer.

*Attention: in accordance with regulation 2003-9 on pool safety, we remind you that this device “must be installed and fastened permanently, all year round”. In the event of drowning while your IMMERSTAR is at a complete stop for whatever reason, neither your vendor nor the manufacturer can be held responsible for the accident.

Warnings:

FROST – Beware: Your IMMERSTAR system will not function if there is water frost inside the sensor, or if the surface of the pool water is frozen. In case of doubt as to the solid or liquid state of the water inside the tube, carry out a functional alarm test.

RIGHTS FOR INTERVENTION – With regard to service and maintenance of this appliance, the only intervention that the user is authorized to perform is change the batteries. For any other intervention, contact your vendor or ACIS if you prefer.

CHECKS – Verify the proper function of your IMMERSTAR regularly by carrying out the triggering tests described in the directions.

Note the results of these tests on the designated sheet in these directions.

In the case of malfunction, protect your pool against access, immediately inform your vendor, or ACIS if preferred, and have the repair procedure initiated.

A test sheet is provided on page 16 of these directions.

Additional Information

Legal Information:

The law N° 2003-9 and the decree on its enforcement N° 2003 1389 were passed in order to counteract the rising number of accidents and drownings in private swimming pools for individual or collective use.

These bills stipulate the following:

As of 1 January 2004, every new, private, open, in-ground swimming pool for individual or collective use must be equipped with a standardized safety device.

As of this date, the manufacturer or installer of such a swimming pool must supply the owner with a technical sheet indicating the received device.

In the case of permanent or temporary transferral of ownership of the IMMERSTAR alarm, it is obligatory to ensure the that the new user is in possession of the entire documents that came with the appliance at the time of initial installation, including the original packaging.

The owners of open in-ground pools for private or collective use installed before 1 January 2004 must have equipped their pool with a standardized safety device by 1 January 2006.

In the case of seasonal rental of the residence, a standardized safety device must be installed before 1 may 2004.

It is essential to insist on active supervision by the parents.

Information Concerning the IMMERSTAR Alarm

The IMMERSTAR alarm system is not a substitute for common sense or for individual responsibility.

It is also not intended as a substitute for supervision by parents and/or responsible adults, who are still the essential factor for the protection of children (most notably those under 5 years of age).

The IMMERSTAR device is an alarm system for open in-ground swimming pools for individual or collective use that indicates a danger (or risk of danger).

The rapid intervention (in under 3 minutes) of a responsible adult is obligatory when the alarm is set off.

The device is made to be installed in pools maximum 12 x 5 m in size (range: 7 metres). Beyond that, we recommend equipping the pool with additional protective measures compliant to the French standard NF P90-307/A1.

The user who turns off the alarm signal must be aware that human supervision must take over.

It is imperative to respond when the signal sounds.

The greatest vigilance of a parent or responsible adult is required in the interval between the end of swimming and reactivation of “surveillance” mode.

In order to reduce the latent period, this mode can also be activated by applying the magnet to the magnetic point.

Switch off the counter-current mechanism when finished swimming in order to be able to reactivate “surveillance” mode.

In no case can your vendor or the manufacturer of the IMMERSTAR alarm be held responsible for the drowning of a child, a dependent person, any adult or any animal.

The installation of an alarm system must not lessen your vigilance or substitute for active supervision of the pool and its surroundings in any case.

This alarm system, as with any other safety device or equipment, is a complementary tool that must be used in the case of momentary absence of surveillance.

Safety Advice:

1 – Supervise and act!

• The surveillance of children must be close and constant

• Designate one person responsible for safety

• Reinforce the supervision if there are multiple users in the pool

• Teach your children to swim from as early an age as possible

• Wet the neck, arms and legs before entering the water

• Learn the rescue procedures, and especially those specific to children

• Forbid diving or jumping in the presence of young children

• Forbid running and animated games at the edge of the pool

• Do not allow a child who does not know how to swim well to enter the pool unaccompanied or without a life jacket or vest.

• Do not leave toys unattended close to or in the pool

• Keep the water permanently clear and sanitary

• Keep water treatment products out of reach of children

• Some counter-current systems prevent the automatic reactivation of the immersion detection system.

• Some cleaning robots of the diving type are incompatible with immersion detection systems

• Take all necessary precautions to prevent children under 5 years of age from accessing the pool when the fault signal sounds, until the device has been repaired.

2 - Have Ready:

An accessible telephone near the pool so as not to leave your children unattended when you use it.

A rubber ring and a pole near the pool.

3 - In the Event of an Accident:

Remove the victim from the water as quickly as possible.

Avoid subsequent accidents: Have the swimmers get out of the water in order to avoid panic and keep them away from the pool.

Alert: Immediately call or alert the emergency services.

Assist: Follow the instructions you are given.

Replace wet clothes with warm, dry covers.

Memorize and put up the numbers of the emergency services near the pool.

Numbers accessible from a landline:

Fire brigade	18 (in France)

Mobile emergency medical service	15 (in France)

Numbers accessible from all telephones:

European emergency number	112

Regional treatment centres for poisoning cases:

| Administrative Region: | Centres for poisoning cases to refer to: | Telephone |
| --- | --- | --- |
| Centre | Angers | 02 41 48 21 21 |
| Pays de la Loire | Angers | 02 41 48 21 21 |
| Aquitaine | Bordeaux | 05 56 96 40 80 |
| Poitou Charentes | Bordeaux | 05 56 96 40 80 |
| Haute Normandie | Lille | "Indigo” N°: 0 825 81 28 22 |
| Nord Pas de Calais | Lille | "Indigo” N°: 0 825 81 28 22 |
| Picardie | Lille | "Indigo” N°: 0 825 81 28 22 |
| Auvergne | Lyon | 04 72 11 69 11 |
| Rhône Alpes | Lyon | 04 72 11 69 11 |
| Corse | Marseille | 04 91 75 25 25 |
| Languedoc Roussillon | Marseille | 04 91 75 25 25 |
| Provence Alpes Côte d'Azur | Marseille | 04 91 75 25 25 |
| Réunion | Marseille | 04 91 75 25 25 |
| Bourgogne | Nancy | 03 83 32 36 36 |
| Champagne-Ardennes | Nancy | 03 83 32 36 36 |
| Lorraine | Nancy | 03 83 32 36 36 |
| Ile de France | Paris | 01 40 05 48 48 |
| Antilles | Paris | 01 40 05 48 48 |
| Guyane | Paris | 01 40 05 48 48 |
| Basse Normandie | Rennes | 02 99 59 22 22 |
| Bretagne | Rennes | 02 99 59 22 22 |
| Alsace | Strasbourg | 03 88 37 37 37 |
| Franche Comté | Strasbourg | 03 88 37 37 37 |
| Limousin | Toulouse | 05 61 49 33 33 |
| Midi-Pyrénées | Toulouse | 05 61 49 33 33 |

Monthly Tests

In order to ensure proper functioning of your IMMERSTAR alarm, it is imperative to test your device every month and to enter the results into the table below.

In the case of malfunction, get in touch with your vendor immediately, or ACIS if you prefer.

Should you ever want to return the device during the warranty period, you may be asked to present this table, duly filled out.

| N° | Date of Test | Success | Fail | Observations |
| --- | --- | --- | --- | --- |
| 1 |  |  |  |  |
| 2 |  |  |  |  |
| 3 |  |  |  |  |
| 4 |  |  |  |  |
| 5 |  |  |  |  |
| 6 |  |  |  |  |
| 7 |  |  |  |  |
| 8 |  |  |  |  |
| 9 |  |  |  |  |
| 10 |  |  |  |  |
| 11 |  |  |  |  |
| 12 |  |  |  |  |
| 13 |  |  |  |  |
| 14 |  |  |  |  |
| 15 |  |  |  |  |
| 16 |  |  |  |  |
| 17 |  |  |  |  |
| 18 |  |  |  |  |
| 19 |  |  |  |  |
| 20 |  |  |  |  |
| 21 |  |  |  |  |
| 22 |  |  |  |  |
| 23 |  |  |  |  |
| 24 |  |  |  |  |

Warranty

Under the existing warranty, ACIS, responsible for the operation of the IMMERSTAR alarm, attests that this product was designed and manufactured according to the directives of the French standard NF P90-307/A1, and is free from material or manufacturing faults, and shall remain so for a period of two (2) years from the date of its purchase.

This warranty includes return service for parts and labour that do not fall under the category of warranty exclusions. Should the product become defective due to a material or manufacturing fault during the warranty period, ACIS shall repair or replace (at its discretion) the appliance or defective parts free of charge. ACIS reserves the right to replace detached parts or defective products with new or revised factory parts or products.

Warranty Exclusions:

• Within 8 days of your purchase, you must fill in the warranty card and return it to ACIS (signed and accompanied by a copy of your receipt) by recommended mail with acknowledgement of receipt, or traceable mail.

ACIS reserves the right to refuse its free warranty in the case that the test sheets, warranty card or invoice cannot be produced, or if the information on these documents is altered, erased, illegible or incomprehensible.

• You must carry out the tests every month for the entire duration of the warranty. We recommend you continue to make this effort even after the warranty has expired.

• The warranty does not apply if the installation is not compliant on all points with that described in this manual.

• Transferral of ownership of an appliance already installed voids the warranty. This exclusion must be made known to the new owner, and shall be treated as accepted by the latter in the case of an accident.

• The warranty does not apply if the serial numbers and elements required for traceability of the appliance on the housing are damaged, faded or rendered illegible.

• The warranty does not cover the following points:

• Periodical maintenance and repair or replacement of wearing parts in the scope of normal use,

• Any adaptation or modification attempting to improve the product compared to its initial performance, which are described in this manual, without prior agreement in writing from ACIS.

• Costs of transport, transport to home or any transport risks directly or indirectly related to the warranty of the IMMERSTAR alarm.

• Damage resulting from:

- Bad use, including (but not limited to) inappropriate use of the device, or failure to observe the instructions of these installation directions,

- Use and maintenance of the product.

- Repairs performed by unauthorized persons or the user.

- Accidents, lightning, flood, fire or any other cause that goes beyond the responsibility of ACIS.

No clause of this warranty is effected by the statutory rights of the user.

After-Sales Return Service

• Any return of the product in terms of a warranty claim must first be accepted by ACIS.

The customer must contact the vendor of his/her immersion detector or ACIS if preferred. If this is recognized as defective, a product return number shall be issued to the customer.

• The product must be returned correctly protected, in its original packaging, to the address indicated, accompanied by the original sales invoice, of which the buyer must keep a copy.

The return number issued to you must appear in legible characters on the packaging, next to the destination address.

Any product without this return number shall be refused. The fees and risks involved in returning the product are at the customer’s expense.

• Upon reception of the immersion detector, we shall perform the necessary tests to verify the fault. In case this test is successful, we shall proceed to exchange or repair the device as promptly as possible.

Neither ACIS nor your vendor is obliged to replace your apparatus unconditionally in the case of immobilization. You must reinforce the active supervision of your pool during this period.

Limits of Responsibility

The responsibility of ACIS in accordance with the existing warranties is limited to the repair or replacement of the IMMERSTAR alarm.

ACIS shall not be obliged to replace or repair the product if the limited contractual warranty as described in the passages above cannot be applied. The responsibility of ACIS for any defective product shall in no case exceed the purchase price of the defective product.

This limitation is valid even if ACIS cannot or will not repair or replace a defective product, and compensation does not correspond with the fundamental purpose. ACIS is in no case responsible for any general, indirect, secondary or special damage.

ACIS has only one duty of care: to supply you with an appliance in working condition, free of material or manufacturing defects. In no case can ACIS or its vendors be held responsible for any fall or drowning of any child, adult or animal.

You remain responsible for the safety of your swimming pool.

The integrated sirens of the immersion detector are compliant with the requirements of the standard NFP 90-307/A1.

In no case can ACIS or its vendors be held responsible in the case of problems related to the sounding of sirens.

Declaration of Conformity

The IMMERSTAR immersion detector has passed the tests related to the standard NFP 90‑307/A1 that apply to alarm systems for swimming pools.

| Immersion Detector | Power Supply |
| --- | --- |
| VisioPool® | (4 x 1.5 V) 6 Volts - DC |

Useful Information

| Survival rate | 100 % |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | 80 | 1 minute | 2 minutes |  |  |  |
|  | 60 |  |  | 3 minutes |  |  |
|  | 40 |  |  |  |  |  |
|  | 20 |  |  |  | 4 minutes |  |
|  | 0 |  |  |  |  | 5 minutes |
|  | Duration of immersion |

For your information, you should know that the duration of immersion exponentially reduces the survival rate (data provided by services dealing with disasters, bomb disposal etc., and used for all official exercises for training these services)

• There is never zero risk:

Only your active supervision combined with the passive surveillance of the IMMERSTAR alarm can assure a decent degree of safety. The installation of this alarm system must not lessen your degree of vigilance or substitute for active, visual vigilance of the pool and its surroundings in any case.

The rapidity of intervention is decisive in the treatment of any accident.

NEVER leave the swimming pool when there is a child or children playing near to it.

15 rue des Marais - 44310 St Philbert de Grand Lieu - FRANCE

Red indicator:

surveillance mode

CONTROL PANEL

Green indicator:

swimming mode

Magnetic zone